Progress review 1

---
H bridge
- Connected to power source DC motor can only in one direction.
- However, controlled through transistor and PWM, motor can spin with variable speed..
- ..but, how to move backwards?
- Solution: H-bridge

---
H bridge
- Principle of an H bridge.
- Replace each switch with a transistor.
- S1 and S4 => IN1.
- S2 and S3 => IN2.
- Truth table:

---
H bridge
In this project, we will use the motor driver l298n (double H bridge for 2 DC motors).

---
H bridge
Circuit

---
Commands from control station
- Use of the keyboard to control the recovery system.
- Implementation of a first version.

---
Commands from control station
- Keyboard map.
- Winch step up/down: ‚q‘ / ‚a‘.
- Turn light on/off: ‚1‘ / ‚2‘.
- Turn camera one step right/left: ‚x‘ / ‚z‘.

---
Commands from control station
- Raise/lower upper claw: ‚r‘ / ‚f‘.
- Raise/lower lower claw: ‚t‘ / ‚g‘.
- Move the car forwards/backwards: ‚i‘ / ‚k‘.
- Turn the car to the left/right: ‚j‘ / ‚l‘ (increasing the speed of one motor and decreasing the speed of the other motor).

---
Commands from control station
- 3 different drive modes: duty cycle up to 255/255 => ‚b‘, duty cycle up to 190/255 => ‚n‘, duty cycle up to 130/255 ‚c‘.
- Spinning the car to the left/right: ‚J‘ / ‚L‘

---
Claw
- Two-part cylindrical claw from a PVC pipe:
- Upper part: 3 quarters.
- Lower part: 1 quarter.
- Opening and closing through two servo motors, one for each part.
- First prototype controlled through an Arduino.
To Buoy
Claw
Camera
Tracks