Progress Seminar
Team 10
Mohamed Regaieg
12/4/2017

---
Driver Interface
Driver Interface
- Use of the keyboard to control the recovery system.
- Implementation of a first version.

---
Driver Interface
Driver Interface
Available resources:
  - send_str(char msg[]);
  - char get_char(void);
  - Keyboard
  - Terminal (Standard text editor)
- Limitation resources:
  - Only one key button can pressed at each moment

---
Driver Interface
Driver Interface
Keyboard map:
Key	Function	Key	Function
q/a	Winch step up/down	y/h/n	Three different speeds
z/x	Turn camera one step left/right	i/m	Move the car forwards/backwards
1/2	Turn light on/off	k	Stop the car
r/f	Raise/lower upper claw	j/l	Turn car left/right
t/g	Raise/lower lower claw	J/L	Spinning the car to the left/right

---
Driver Interface
Driver Interface
Feedback to the driver: after any change the system status will be printed in the terminal:
  - Positions of the servo
  - Duty cycle and direction of each DC motor
  - Light state
  - Integration of stepper movement for the next version

---
Driver Interface
Driver Interface
Upcoming tasks
  - Validation with the whole system
  - Adjusting the control speed of the car
  - Adjusting the stepwise movement of the servos and the stepper
  - Improving the feedback

---
Claw Design

---
Needed parts:
  - 1 Pipe
  - 2 pipe caps
  - 4 hinges
  - 2 servo motors
  - 1 aluminium plate sheet
  - 4 M4 x 25mm bolts and their nuts
  - 6 M3 x 15 bolts and their nuts

---
The PVC pipe: DN100 SN6
  - Inner diameter 104 mm
  - Large enough:
    - larger than the widest section of the submarine (72 mm)
    - Submarine can be inclined (approximately 100 mm are needed)
  - Used length 300 mm, split into
    - One quarter: lower claw part
    - 3 quarters: upper claw part.

---
Servo motors
  - Torque calculation: assumptions
    - One rock is grabbed with the submarine
    - Servo pipe connection at 1 cm from the servo axis
    - The whole load is acting at the furthest point
      - 100 mm for the upper claw part
      - 50 mm for the lower claw part
    - System underwater (Buoyancy against gravity)
    - Considered loads:
      - Pipe + caps
      - Submarine
      - Rock

---
Servo motors
  - Torque calculation: results:
    - Upper claw: 2.5 Kgcm
    - Lower claw: 5 Kgcm
  - Selected motor MG995
    - Torque is large enough for this application (13-15 kgcm)
    - Used by wide community
    - Very cheap ($5)

---
Aluminium plate
  - Torque calculation
    - Assumptions:
      - Plate is rectangular with 3 mm thickness
      - Holes are neglected
      - System underwater (Buoyancy against gravity)
    - Results
      - Maximum stress = 3 MPa = 0.03 yield stress
      - Strain = 4 10^-5

---
Motor pipe attachment:
  - Position the motor arm between two aluminium pieces attached to the pipe
  - Still need torque calculation
  - Alternative
    - One aluminium parts attached the servo arm (Bolts M1.6)
    - two aluminium pieces attached to the pipe

---
Cost estimation

---
Further calculations
  - Weight of the whole claw : 1.3 Kg
  - Buancy of the whole claw: 6.13 N

---
Upcoming tasks
  - Waiting for the aluminium parts from Doug (The waiting list seems to be extremely long)
  - Cutting the pipe at the STC
  - Waiting for the motors (they should be here at most by the end of next week)
  - Connect the servo to the plate ($8 are available for that)
  - Buy the caps, cut them and attach them to the claw
  - Waterproofing the servos ($5 Graisse and Plasti Dip)